## Slide 1: Question 223.18.4
What is the power (in Diopters) of a lens with a focal distance of 0.5m?
5
4
3
2
1

## Slide 2: Simple Magnifier
A simple magnifier consists of a single converging lens
This device is used to increase the apparent size of an object
The size of an image formed on the retina depends on the angle subtended by the eye

## Slide 5: The Size of a Magnified Image
When an object is placed at the near point, the angle subtended is a maximum
  The near point is about 25 cm
When the object is placed near the focal point of a converging lens, the lens forms a virtual, upright, and enlarged image

## Slide 6
d

## Slide 7: Angular Magnification
Angular magnification is defined as
The angular magnification is at a maximum when the image formed by the lens is at the near point of the eye
  s’ = - 25 cm
  Calculated by

## Slide 8: Angular Magnification, cont.
The eye is most relaxed when the image is at infinity
  Although the eye can focus on an object anywhere between the near point and infinity
For the image formed by a magnifying glass to appear at infinity, the object has to be at the focal point of the lens
The angular magnification is

## Slide 9: Magnification by a Lens
With a single lens, it is possible to achieve angular magnification up to about 4 without serious aberrations
With multiple lenses, magnifications of up to about 20 can be achieved
  The multiple lenses can correct for aberrations

## Slide 10: The Compound Microscope

## Slide 11: Compound Microscope

## Slide 12: The telescope

## Slide 14: Refracting Telescope

## Slide 15: Reflecting Telescope: Newtonian

## Slide 16: Examples of Telescopes
Reflecting Telescopes
  Largest in the world are the 10-m diameter Keck telescopes on Mauna Kea in Hawaii
    Each contains 36 hexagonally shaped, computer-controlled mirrors that work together to form a large reflecting surface
Refracting Telescopes
  Largest in the world is Yerkes Observatory in Williams Bay, Wisconsin
    Has a diameter of 1 m

## Slide 17: Resolution

## Slide 18: Question 223.19.1
Resolution is
The ending argument in a debate
The ability to distinguish separate point sources in an optical image
The distance between bright fringes in a diffraction pattern
The distance between dark fringes in a diffraction pattern

## Slide 19: Question 233.19.2
Cat’s eyes have pupils that can be modeled as vertical slits. At night, would cats be more successful in resolving
Headlights on a distant car
Vertically separated lights on the mast of a distant boat?

## Slide 22: Resolution

## Slide 23: Resolution
The ability of optical systems to distinguish between closely spaced objects is limited because of the wave nature of light
If two sources are far enough apart to keep their central maxima from overlapping, their images can be distinguished
  The images are said to be resolved
If the two sources are close together, the two central maxima overlap and the images are not resolved

## Slide 26: Resolved Images, Example

## Slide 27: Barely Resolved, Example

## Slide 28: Images Not Resolved, Example

## Slide 29: Resolution
The ability of optical systems to distinguish between closely spaced objects is limited because of the wave nature of light
If two sources are far enough apart to keep their central maxima from overlapping, their images can be distinguished
  The images are said to be resolved
If the two sources are close together, the two central maxima overlap and the images are not resolved

## Slide 33: Resolution, Rayleigh’s Criterion
When the central maximum of one image falls on the first minimum of another image, the images are said to be just resolved
This limiting condition of resolution is called Rayleigh’s criterion

## Slide 34: Resolution, Rayleigh’s Criterion, Equation
The angle of separation, θmin, is the angle subtended by the sources for which the images are just resolved
Since λ << a in most situations, sin θ is very small and sin θ » θ
Therefore, the limiting angle (in rad) of resolution for a slit of width a is
To be resolved, the angle subtended by the two sources must be greater than θmin

## Slide 35: Circular Apertures
The diffraction pattern of a circular aperture consists of a central bright disk surrounded by progressively fainter bright and dark rings
The limiting angle of resolution of the circular aperture is
  D is the diameter of the aperture

## Slide 36: Circular Apertures, Well Resolved
The sources are far apart
The images are well resolved
The solid curves are the individual diffraction patterns
The dashed lines are the resultant pattern

## Slide 37: Circular Apertures, Just Resolved
The sources are separated by an angle that satisfies Rayleigh’s criterion
The images are just resolved
The solid curves are the individual diffraction patterns
The dashed lines are the resultant pattern

## Slide 38: Circular Apertures, Not Resolved
The sources are close together
The images are unresolved
The solid curves are the individual diffraction patterns
The dashed lines are the resultant pattern

## Slide 39
Completely Resolved
Rayleigh Criterion
Sparrow Criterion
Unresolved

## Slide 40: Resolution, Example
Pluto and its moon, Charon
Left: Earth-based telescope is blurred
Right: Hubble Space Telescope clearly resolves the two objects
Pluto
Charon